## Slide 2
Realtime perception of an autonomous Racecar
Tobias Bosl
Tjorven Burdorf
Vincent Guttmann
Lukas Kraft

## Slide 3: Our Project
Perception of an autonomous racecar
Camera based
Using Yolov8
Basis for localization and trackplanning

## Slide 4
Driverless Architecture

## Slide 5
Detection
Projection
Main Components

## Slide 6: Prerequisites - Hardware
Driverless computer
Camera

## Slide 7: Prerequisites - FSOCO dataset
Shared Dataset for fomular students
For cone detection

## Slide 8: Prerequisites - TensorRT
Ecosystem developed by NVIDIA
Optimizes neural networks for fast inference
Builds it‘s own TensorRT Engine

## Slide 9: Implementation - creating Model
Train Yolov8 on FSOCO dataset
960 x 960 pixel
FP16
Convert trained .pt file over .onnx to seriealized .engine

## Slide 10: Implementation - Preprocessing
Crop both images to 2:1 format
Combining both camera images vertically
Change colormode to BGR
Flatten the data to a float vector
Normalize the float vector

## Slide 11: Implementation - Infer

## Slide 12: Implementation - Postprocessing
Delete redundant boxes via Non Maximum suppresion
  Sort list by confidence
  Calculate intersection
  Remove boxes with too much overlap
Assign bounding boxes to image
Recalculate boundingbox coordinates

## Slide 13: Implementation - Projection
Why Project Cones into the Real World?
Camera sees 2D image
autonomous driving requires 3D understanding
Cones mark the track boundaries
→ vehicle must estimate their relative distance and lateral position
Input: 2D bounding box → Output: cone position in vehicle coordinates

## Slide 14: Depth and Angle Estimation from a Camera Image
Combine with angle between cone and current car orientation → triangle
Performance matters → no access to depth map from camera
Projection must rely on visual features like:
  Cone height and width in pixels
  Distance from bounding box to image borders
  Position of bounding box center
Real-world cone height known → allows simplified model

## Slide 15: Improving Angle Accuracy with Undistortion
Raw projection can be inaccurate due to lens distortion
Angle between driving orientation and cones is distorted towards image border
Applied OpenCV undistortion using calibration matrix and distortion coefficients
This allows to calculate the angle between car orientation and cone more presicely

## Slide 16: Problems Regarding Distance Estimation
Bounding boxes do not have same ratio between height and width always

## Slide 17: Depth Estimation
Due to the problems just listed precise calculation almost impossible
Tested three approaches to find the closest results based on
  Height and width of bounding box compared to height and width of actual cone
  Distance between lower bounding box border and lower image border
  Pinhole-Based Distance Estimation
Neither of them was good alone
All had some spots with better and some with worse quality

## Slide 18: Optimizing the Results
Error observed between calculated and actual distances
Linear regression to adjust outputs based on real measurements
Result: Weighting the three approaches differently to get closer to the actual position

## Slide 19: Demonstration